## Slide 1
A Hybrid ROS 2 Architecture for a TurtleBot 4 Robot Tour Guide
Landmark recognition + deliberative tour planning + classified recovery for indoor tours
Robot Tour Guide Team | OU TurtleBot 4 | ROS 2 Jazzy + Gazebo Harmonic | Nav2 + OpenCV ArUco
OU
TurtleBot
Tour
HYBRID
ROBOTICS
POSTER
Learning Objectives
Design a hybrid robot architecture for a tour-guide mission.
Integrate perception, planning, Nav2 execution, narration, and recovery.
Abstract
Problem
A waypoint follower does not know when to narrate, wait, replan, or skip a blocked stop.
Interest
A tour guide must look purposeful around people and changing furniture.
Approach
A hybrid ROS 2 stack combines ArUco landmarks, a decayed world model, TSP-style planning, Nav2, and TTS.
Answer
The executive selects recoveries for person blocking, moved furniture, closed doors, unreachable POIs, and unknown failures.
Conclusion
Mission-level reasoning can improve tour behavior without replacing Nav2.
Introduction
Motivation: indoor tour robots need navigation plus recognizable, human-facing behavior.
Nature: a ROS 2 Python package that runs above TurtleBot 4 bringup and Nav2.
Scope: classroom-scale tours in REPF B4 using the stock OAK-D camera and LiDAR.
Approach: deliberative POI ordering, executive state machine, reactive safety monitor.
Result overview: 8 ROS nodes, 3 launch paths, YAML-configured landmarks and POIs.
Conclusion preview: simple symbolic landmarks make the tour reliable and explainable.
Related Work
The design follows layered/hybrid robot-control ideas (Brooks), uses ROS 2 Jazzy and Nav2 for navigation, and uses OpenCV ArUco markers for robust symbol-to-description landmark recognition.
Why This Is Different
Nav2 still handles path planning and control; this project adds the mission layer: plan tour order, confirm arrivals with markers, narrate stops, and classify why navigation failed.
Architecture and Data Flow
Perception
World + Planning
Execution
OAK-D
RGB + camera_info
aruco_detector
OpenCV ArUco
/landmarks/detected
JSON
LiDAR /scan
+ optional YOLO
semantic_perception
people, furniture,
door gaps
/world/objects
JSON
world_model
half-life decay
RViz markers
fuses
pois.yaml
landmarks.yaml
params.yaml
tour_planner
nearest-neighbor
+ 2-opt
/tour/current_plan
JSON
executive
state machine
failure classifier
Nav2
NavigateToPose
narrator
TTS + terminal
safety_monitor
zero cmd_vel
goals
speech
Methods
1 Print markers
4x4 ArUco ids match landmark descriptions.
2 Map POIs
Replace placeholder x, y, yaw with map-frame poses.
3 Plan tour
Nearest-neighbor route refined with 2-opt.
4 Execute
Nav2 drives; ArUco can confirm arrival early.
5 Recover
World snapshot classifies failure and chooses action.
Failure Classifier
World signal
Class
Recovery behavior
Person within 1.5 m
PERSON_BLOCKING
Say "Excuse me", wait, retry.
New furniture-class object
FURNITURE_MOVED
Request replan from current pose.
No door-open hint after retries
DOOR_CLOSED
Drop POI and narrate skip.
Retries exhausted
POI_UNREACHABLE
Drop POI and continue tour.
No clear signal
UNKNOWN
Pause briefly and retry once.
Appendix / Reusable Code
Reusable by other teams: aruco_detector, landmark_announcer, tour_planner, plus YAML schemas for landmarks and POIs. Source, launch files, and run instructions are in README and appendices.
Results
Implemented evidence
Result
ROS 2 nodes
8 runtime nodes
Launch paths
full, sim wrapper, perception-only
Tour data
4 configured POIs and 4 landmark records
Recovery classes
5 mission-level outcomes
Syntax check
all node files passed py_compile
Demo note
real robot metrics still need final run data
Demonstration Behavior
ArUco-only path: teleoperate near a marker; robot announces the matching landmark with dwell and cooldown.
Full tour path: planner orders POIs; executive sends Nav2 goals; landmarks confirm arrival; narrator speaks descriptions.
Obstacle path: failures are interpreted as person blocking, moved furniture, closed door, unreachable POI, or unknown.
Discussion
Notable points: the system adds symbolic tour context above Nav2 instead of replacing navigation. This matched expectations: ArUco markers give reliable, inspectable arrival evidence, and the executive can make recoveries legible to an audience. Compared with generic layered control, the layers here are mission-specific: tour order, landmark confirmation, narration, and recovery are explicit.
Conclusions
Hybrid design is justified: deliberative planning, executive recovery, and reactive safety operate on different time scales.
A small symbolic landmark database is enough to make narration data-driven and reliable in a constrained tour space.
Future Work
Collect final run metrics; track visited POIs during replans; ignore stale Nav2 cancellation results after marker-confirmed arrival; improve camera-LiDAR fusion; add richer visitor interaction.
Bibliography: Brooks 1986; Garrido-Jurado et al. 2014; ROS 2 Jazzy docs; Nav2 API docs; OpenCV ArUco docs; TurtleBot 4 user manual.